## Slide 1: A Robot Task Planner that Merges Symbolic and Geometric Reasoning
Elective in Artificial Intelligence
Reasoning Agents
Leandro Maglianella - 1792507
Prof. Fabio Patrizi

## Slide 2: Paper Content
This paper is about aSyMov, a planner designed to address intricate robot planning problems where geometric constraints are relevant and influence the symbolic plan.
The proposed implementation of aSyMov is tested on an illustrative example.

## Slide 3
Problem Description

## Slide 4: Problem Description
Often planners lack of effectiveness in robotics task because there is a gap between the representation they are based on and the physical world.
At each step of the planning process both symbolic and geometric constraints must be considered.

## Slide 5: Problem Description
The authors create an example based on the Hanoi Tower Problem.
“Classical” Hanoi Tower Problem

## Slide 6: Problem Description
“Geometric Hanoi Tower Problem with 3 disks” (GHTP-3)
Disks are moved by a non-holonomic robotized fork-lift.

## Slide 7: Problem Description
A good symbolic planner would be able to find the optimal solution:
BUT this solution is actually not achievable in our case because the environment is also geometrically constrained.

## Slide 8: Problem Description
All possible robot motions depend not only on the static environment but on the context (robot and objects positions).
Each context may possibly create a different free-space topology and consequently create specific constraints on robot motions.

## Slide 9
Implementation

## Slide 10: Geometric Reasoning
Environment: 3D-world with static and dynamic components.
Roadmap: The motion planner uses a Probabilistic Roadmap method.
In the constructed graph, a node represents a collision-free configuration and the edges are valid robot motions.

## Slide 11: Geometric Reasoning
A solution to a manipulation problem is a sequence of transit and transfer motions.
Transit / Transfer / Placement:
The set of all stable object positions is called placement.
The transit motion of the robot between two grasping positions.
The transfer motion of the robot with a taken object.

## Slide 12: Symbolic Reasoning
A symbolic position
P_R_TI_TA_O: the configurations where a robot R can grasp an object O.
In the figure = {N1, N2}.
P_R-O_TA_TI: the configurations where a robot R can drop an object O.
In the figure = {N4, N5}.
P_R_TI_RELOAD_BATTERY: the configurations where a robot R can apply a RELOAD_BATTERY action.
A subset of the configuration nodes of one roadmap that satisfy a given property.
P_{robot name}_{roadmap name}_{property}

## Slide 13: Symbolic Reasoning
The authors chose to use PDDL 2.1 to specify the described symbolic representation.
(composed ?r1 ?r2 ?r3)
(belongs-to ?p ?r ?roadmap-type)
(has-purpose ?p ?pos-type)
(connection ?p1 ?p2)
(on ?r ?p)
Basic predicate set:
(goto ?r ?p1 ?p2)
(grasp ?r ?p1 ?o ?p2 ?new-r ?p3)
(release ?old-r ?p1 ?o ?p2 ?r ?p3)
(switch-motion ?r ?p1 ?p2)
Basic action set:

## Slide 14: Algorithms and Strategies
Extend state algorithm

## Slide 15
Experiments

## Slide 16: Experimental Instances and Results
(3)
 | CPU time | Nb step | Connectivities | Plan length
(1) | 0.266 | 38.5 | 17.5 | 28
(2) | 9.97 | 63.7 | 25.4 | 28.8
(3) | 271.6 | 243.8 | 71.2 | 44
(4) | 298.9 | 213.6 | 62.8 | 40.16

## Slide 17: Experimental Instances and Results

## Slide 18
Final Personal Comment

## Slide 19: Final Personal Comment
Remarkable research and results, especially being it from 2004.
We intend to make a project about a robot that act as a teacher, therefore not colliding with children while moving an object is a plus.
Generated plans take into account the geometric consequences of robots’ actions.
Plans have a better chance to be valid in the real world.

## Slide 20: References
Stephane Cambon, Fabien Gravot and Rachid Alami
  "A Robot Task Planner that Merges Symbolic and Geometric Reasoning", 2004
  Proceedings of the 16th Eureopean Conference on Artificial Intelligence, ECAI'2004

## Slide 21: Appendix